## Slide 1
Sparse and Redundant Representations and Their Applications in
Signal and Image Processing (236862)
Section 3: Image Denoising
Winter Semester, 2018/2019
Michael (Miki) Elad

## Slide 2
Meeting Plan
Quick review of the material covered
Answering questions from the students and getting their feedback
Discussing a new material – Facial Image Compression
Administrative issues

## Slide 3
Overview of the Material
Image Denoising – The Sparseland Way
  The Denoising Problem and its Importance
  First Steps in Image Denoising
  Variations on the Global Thresholding Algorithm
  SURE for Parameter Tuning: The Theory
  SURE for Parameter Tuning: The Practice
  Patch-Based Denoising – Basics
  Patch-Based Denoising: Theoretical Foundations
  The K-SVD Image Denoising Algorithm
  Patch-Based Denoising – Other Methods
  Image Denoising - Summary

## Slide 4
Your Questions and Feedback
Question: L2 – Good or Bad?
The message in this course about the suitability of the L2 seems to be confusing. When discussing Wiener filter, L2 was said to be a bad option, yet in defining pursuit algorithms we keep using L2. Now, when discussing denoising, we are aiming to get a minimal L2 error. So, what is the bottom line: L2 – bad or good?
Answer: Sorry for the confusion – lets put some order to this picture. We use the L2 in three very different contexts, each with it’s own story:
L2
Here the L2 represents the knowledge that the noise is white & Gaussian – this is well-justified
Here the L2 is used as a prior on the representation, causing a spread of the non-zeros everywhere - something that we know to be a VERY BAD choice
This is the Mean-Squared-Error between the recovered and the original image. While there are some attacks on this option, it is still important and popular
&

## Slide 5
Your Questions and Feedback

## Slide 6
New Material?
Face Image Compression
  Here is a chapter that we omitted from the MOOC after a debate, despite its importance and elegance: image compression using the Sparseland model
  Rather than discussing general purpose compression, we focus on a specific family of images – frontal faces
  This work is a brilliant MSc research by Ori Bryt

## Slide 7
Administrative Issues
Lets talk about:
Please provide your feedback to the Technion’s course 236862 (MISHAAL HAMARTZE) & especially with free text comments
Remember the deadline on the 6th for the course mid-project